N/A = Not Applicable                                      		MATERIAL SAFETY DATA SHEET                                       	Effective Date:  OCT 2002

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 1 - PRODUCT IDENTIFICATION				   Revised Date: MARCH 2008

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Product Name: METAL SAFE CTC 		  Product ID#: 154022          	HMIS SYMBOL     		HMIS   NFPA      		NFPA SYMBOL

Generic Name: Truck Cleaner 						HEALTH        |2|   	            SEVERE 4 EXTREME   		FIRE        |0|

Supplier's Name: BIRSCH INDUSTRIES, INC. 				FLAMMABILITY  |0|           SERIOUS 3 HIGH      		REACTIVITY  |2|

Supplier's Address: 476 Viking Drive, Suite 102 				REACTIVITY    |2| 	     MODERATE 2 MODERATE  	TOXICITY    |2|

Virginia Beach, VA  23452						             SLIGHT 1 SLIGHT    		SPECIAL     |1|

Emergency Phone Number: (800) 255-3924							          MINIMAL 0 INSIGNIFICANT

Information Phone Number: (757) 622-0355

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 2 - INGREDIENTS

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

CHEMICAL NAME                                       	CAS #           	WT. %                       TWA-TLV             	STEL-TLV        	CARCINOGEN

MG/M3               	MG/M3

Dodecylbenzine Sulfonic Acid                     		27176-87-0        	< 3.0                          N/A                 	N/A                          	No

*Phosphoric Acid                                   		7664-38-2        	<16.0                       	1                   	3                           	No

*Oxalic Acid                                        		144-62-7        	< 6.0                           1                   	2                           	No

Water                                             		7732-18-5       	to 100                         N/A                 	N/A                          	No

*This product contains toxic chemicals subject to

the reporting requirements of section 313 of the Emergency Planning

and Community Right-To-Know Act of 1988 and of 40 CFR 372.

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 3 - PHYSICAL DATA                              	|                            SECTION 4 - FIRE AND EXPLOSION HAZARD DATA

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Boiling Point (F): >212o F     		Specific Gravity: 1.15                     	| Flash Point (Method Used): N/A

Vapor Pressure: 20 mm Hg @68oF 	Vapor Density:      (Air=1): >1            	| Upper Explosive Limit: None

% Volatile: 85                		pH: 1.5                                    		| Extinguishing Media: N/A

Solubility in Water: Complete 		Evaporation Rate:   (Water=1): <1          	| Special Fire Fighting Procedures: N/A

Physical Description: Blue water thin liquid with a mint odor.           		| Unusual Fire & Explosion Hazards: Reacts with metals to liberate Hydrogen

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 5 - REACTIVE DATA                             		|        	    SECTION 6 - STORAGE AND HANDLING INFORMATION

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Stability: Stable          Hazardous Polymerization: Will not occur      		| Precautions to be Taken in Handling and Storage: Do not stack cases or pails

Incompatibility (Materials to Avoid): Metals and other chemicals         		| over three high. Avoid inhalation of vapors or mist. Avoid all personal contact

Hazardous Decomposition Products: None                                   			|

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 7 - HEALTH HAZARDS AND FIRST AID

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Effects of Overexposure                                                  			| First Aid Procedures

Primary Route of Entry:						|

Skin: Severe skin irritant. May cause reddening, swelling, and        		| Skin: Flush with water. Seek medical attention if irritation persists.

possible skin damage.                                           			|

Eyes: Severe eye irritant. Liquid and mist may damage eyes, causing   		| Eyes: Flush with large quantities of water, holding eyelids open. Seek medical

corneal damage.                                                 				|           attention if irritation persists.

Inhalation: Vapors and mist may be irritating to mucous membranes in  		| Inhalation: Get to fresh air. Seek medical attention if irritation persists.

the throat, and lungs.                                          			|

Ingestion: Irritating and corrosive to the mouth and throat. May      		| Ingestion: Do not induce vomiting. Drink large quantities of water. Seek

cause headache, nausea, abdominal pain, vomiting and diarrhea.  	|       	 medical attention immediately.

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 8 - SPECIAL PROTECTION INFORMATION

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Respiratory Protection: Use in well ventilation area.                    			| Ventilation: Provide local exhaust to keel TLV of Section 2 ingredients below

|       	    acceptable limit.

Protective Gloves: Acid Proof                                            			| Eye Protection: Safety glasses.

their Protective Equipment: Rubber aprons & rubber shoes 			|

PLEASE READ AND FOLLOW THE DIRECTIONS ON THE PRODUCT LABEL.  THEY ARE YOUR BEST GUIDE FOR THIS PRODUCT IN THE MOST EFFECTIVE WAY, AND THEY ALSO GIVE THE NECESSARY SAFETY PRECAUTIONS TO PROTECT YOUR HEALTH.

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 9 - SPILL OR LEAK PROCEDURES

--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Steps to be Taken in Case Material is Released or Spilled: Sprinkle      		| Waste Disposal Method: In accordance with all applicable Federal, State and

hydrated lime or soda ash on spill area. Scrape up and remove. For small 		| Local regulations.

spills, dilute with water and mop up. Wear gloves and goggles always.    		|

US DOT INFORMATION

PHOSPHORIC ACID SOLUTION

8,UN1805, PGIII