N/A= Not Applicable			MATERIAL SAFETY DATA SHEET		EFFECTIVE DATE:OCT 2002

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

SECTION 1-PRODUCT IDENTIFICATION	                  Revised Date: July 2004

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Product Name: SRS STRIPPER 	Product ID#: 174755		HMIS SYMBOL	        HMIS   NFPA	        NFPA SYMBOL

Generic Name: Stripper 				HEALTH	2	  SEVERE 4 EXTREME    FIRE 1

Supplier’s Name: BIRSCH INDUSTRIES			FLAMMIBILITY 1	SERIOUS 3 HIGH	        REACTIVITY 0

Supplier’s Address: 476 Viking Drive, Suite 102		REACTIVITY 0   MODERATE 2 MODERATE  TOXICITY 2

Virginia Beach, VA  23452					  SLIGHT 1 SLIGHT	         SPECIAL 0

Emergency Phone Number: (800) 255-3924				                MINIMAL 0 INSIGNIFICANT

Information Phone Number: (757) 622-0355

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 2-INGREDIENTS

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Chemical Name		    CAS#		WT.	TWA-TLV	STEL-TLV	CARCINOGEN

MG/M3		MG/M3

*Caustic Soda		    1310-73-2	<2.0	2C		N/A		NO

*Ethylene glycol monobutyl ether     111-76-2	<5.0	121		N/A		NO

*Monoethanolamine		      141-43-5	<1.0	N/A		N/A		NO

EDTA			  26027-38-3	<1.0	N/A		N/A		NO

Water			        60-00-4	<1.0	N/A		N/A		NO

*This product contains toxic chemicals subject to

the reporting requirements of Section 313 of the

Emergency Planning and Community Right-To –Know Act

of 1988 and of 40 CFR 372.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 3- PHYSICAL DATA				SECTION 4- FIRE AND EXPLOSION HAZARD DATA

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Boiling Point (F): 212 oF	Specific Gravity: 1.06			Flash Point (Method Used): 205o

Vapor Pressure: 20mm 	Vapor Density: (Air =1):>1		Upper Explosive Limit: N/A

% Volatile: 90		pH:13.0				Extinguishing Media: CO2 in Water

Solubility in water: Yes	Evaporation Rate: (Water=1):<1		Special Fire Fighting Procedures: None

Physical Description: Water thin yellow liquid with a butyl smell		Unusual Fire & Explosion Hazards: None

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 5-REACTIVE DATA				SECTION 6- STORAGE AND HANDLING INFORMATION

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Stability: Stable	Hazardous Polymerization: Will not occur	Precautions to be Taken in Handling and Storage: Keep out of

Incompatibility (Materials to Avoid): Do not mix with other 	reach of children.  For use by trained personnel only.  Keep

chemicals. 						Container closed during storage.  For institutional and industrial

Hazardous Decomposion Products:  Alkaline vapors in a fire.	Use only.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 7-HEALTH HAZARDS AND FIRST AID

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Effect of Overexposure				First Aid Procedures

Primary Route of Entry:

Skin: Severe skin irritant.  May cause reddening, swelling,	Skin: Flush with water.  Seek medical attention if irritation

and possible skin damage.				persists.

Eyes: Severe eye irritant.  Liquid and mist may damage eyes,	Eyes: Flush with large quantities of water, holding eyelids open.

causing corneal damage				Seek medical attention if irritation persists.

Inhalation:  Vapors and mist may be irritating to mucous	Inhalation:  Get to fresh air.  Seek medical attention if irritation

Membranes in the throat, and lungs.			persists.

Ingestion: Irritating and corrosive to the mouth and throat.	Ingestion:  Do NOT induce vomiting.  Drink large quantities of

may cause headache, nausea, abdominal pain, vomiting		water.  Seek medical attention immediately.

and diarrhea.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 8-SPECIAL PROTECTION INFORMATION

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Respiratory Protection: Use in well ventilated area.		Ventilation: Provide local exhaust to keel TLV of ingredients

Protective Gloves: Waterproof				Eye Protection: Safety glasses.

Other Protective Equipment:  Rubber aprons & shoes.

PLEASE READ AND FOLLOW THE DIRECTIONS ON THE PRODUCT LABEL.  THEY ARE YOUR BEST GUIDE FOR THIS PRODUCT IN THE MOST EFFECTIVE WAY, AND THEY ALSO GIVE THE NECSSARY SAFETY PRECAUTIONS TO PROTECT YOUR HEALTH.

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

# SECTION 9-SPILL OR LEAK PROCEDURES

-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Steps to be Taken in Case Material is Released or Spilled: Mop		Waste Disposal Method: Any method in accordance

Up or otherwise absorb and hold for disposal.			with applicable laws.